KW160 A.T.U.          Construction details

Enclosure – internal dimensions :

Length = 283mm        Width = 152mm        Height = 124mm

Material   1/16” Aluminium

Front panel

152 x 125mm

Rear panel

152 x 70mm

Coil  L1

34 turns        Length = 70.5mm        Internal diameter = 49.5mm

Tinned copper wire  1/16” diameter

Tapped in 10 places = every 3 turns  (wire is indented at tapping point to allow soldering)

Measured total inductance = 16.2µH